## Slide 1: Lecture 00 – Introduction to Computer Architecture
Dr. Matthew Morrison
Assistant Teaching Professor
University of Notre Dame
January 16, 2024
1

## Slide 2: An Introductory Case Study
Let’s compare the run time of a while loop counting to 1,000,000,000
  C vs Python
What do you think will happen?

## Slide 3: Scooter Computer and Mr. Chips

## Slide 4: Time Comparison

## Slide 5: Think, Pair, and Share
When would you want to use Python in your programming?
When would you want to use C in your programming?
When would you want to use Assembly Language in your programming?

## Slide 6: The Concept of a Computer

## Slide 7: In the News
Source

## Slide 8: In the News
Source

## Slide 9: A look under the hood
Let’s look at what happens when we generate assembly language
  gcc –S loop.c
  python –m dis loop.py
C runs directly in the local machine architecture
Python runs in the Virtual Machine

## Slide 10: Abstractions in Programming
Hackers attack Casino’s fish tank thermometer to obtain sensitive data

## Slide 11: Why this course: Computer Security
Spectre, Meltdown
  Likely tens of billions of dollars impact
Stealing Intel encryption keys
Unlocking features in Tesla
Prof. Morrison’s Patent

## Slide 12: Why this course: Custom Silicon
Notes: https://www.cnet.com/tech/computing/google-developing-its-own-arm-based-processors-for-chromebooks-report-says/
https://www.cnbc.com/2021/09/06/why-tesla-apple-google-and-facebook-are-designing-their-own-chips.html
https://www.theregister.com/2022/01/13/microsoft_apple_chip_expert/
https://www.apple.com/newsroom/2020/06/apple-announces-mac-transition-to-apple-silicon/
https://siliconangle.com/2023/07/06/googles-first-fully-custom-pixel-smartphone-chip-delayed-2025/

## Slide 13: Why this course: Custom Silicon
Notes: https://www.cnet.com/tech/computing/google-developing-its-own-arm-based-processors-for-chromebooks-report-says/
https://www.cnbc.com/2021/09/06/why-tesla-apple-google-and-facebook-are-designing-their-own-chips.html
https://www.theregister.com/2022/01/13/microsoft_apple_chip_expert/
https://www.apple.com/newsroom/2020/06/apple-announces-mac-transition-to-apple-silicon/
https://siliconangle.com/2023/07/06/googles-first-fully-custom-pixel-smartphone-chip-delayed-2025/

## Slide 14: Why this course: Custom Silicon
Notes: https://www.cnet.com/tech/computing/google-developing-its-own-arm-based-processors-for-chromebooks-report-says/
https://www.cnbc.com/2021/09/06/why-tesla-apple-google-and-facebook-are-designing-their-own-chips.html
https://www.theregister.com/2022/01/13/microsoft_apple_chip_expert/
https://www.apple.com/newsroom/2020/06/apple-announces-mac-transition-to-apple-silicon/
https://siliconangle.com/2023/07/06/googles-first-fully-custom-pixel-smartphone-chip-delayed-2025/

## Slide 15: Why this course: Custom Silicon
Notes: https://www.cnet.com/tech/computing/google-developing-its-own-arm-based-processors-for-chromebooks-report-says/
https://www.cnbc.com/2021/09/06/why-tesla-apple-google-and-facebook-are-designing-their-own-chips.html
https://www.theregister.com/2022/01/13/microsoft_apple_chip_expert/
https://www.apple.com/newsroom/2020/06/apple-announces-mac-transition-to-apple-silicon/
https://siliconangle.com/2023/07/06/googles-first-fully-custom-pixel-smartphone-chip-delayed-2025/

## Slide 16: Under the C…

## Slide 17: Why Computer Architecture?
What are your current opinions on this course?
Why do you think you are required to take this class?
Let’s put all these thoughts on the board

## Slide 18: What is Computer Architecture?
Story Time: Intel interview

## Slide 19: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 20: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 21: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 22: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 23: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 24: What is Computer Architecture?
Computer Architecture
  System attributes of a computer that contribute to its logical execution and are visible to the programmer
    Instruction set
    Data representation
    I/O mechanisms
    Memory addressing

## Slide 25: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 26: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 27: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 28: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 29: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 30: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 31: What is Computer Architecture?
Computer Organization
  Physical details of a computer that are transparent to the programmer
    Hardware implementation of an instruction
    Control signals
    Memory technology (cache, virtual)
    ALU/CPU/CU designs
  Transparent - a computing process or interface functioning without the user being aware of its presence
  Not Invisible

## Slide 32: What is Computer Architecture?
Problem 1 on HW 1, Exam 1, and the Final Exam
“Define and differentiate between computer architecture and computer organization and give examples of each.”

## Slide 33: Recall from Logic Design
Albacore Architecture
What are the 5 stages of operation?

## Slide 34: Recall from Logic Design
Instruction Fetch
  Gets a compiled binary machine code instruction from the instruction memory, and loads it into the datapath

## Slide 35: Recall from Logic Design
Instruction Decode
  Decodes the machine instruction, and generates the control signals, determines the appropriate registers and memory locations, and the necessary operations to complete the instruction

## Slide 36: Recall from Logic Design
Execute
  Performs the operation dictated by the machine instruction

## Slide 37: Recall from Logic Design
Data Memory
  Performs the operation dictated by the machine instruction

## Slide 38: Recall from Logic Design
Write Back
  If the operation dictates that some information must be stored in temporary registers, it will be done at this stage

## Slide 39: Computer Architecture Catalog Description
Introduction to basic architectural concepts that are present in current scalar machines, together with an introduction to assembly language programming, computer arithmetic, and performance evaluation.
Commercial computer-aided-design software is used to deepen the student's understanding of the top-down processor design methodology. MIPS-based assembly language will be used.

## Slide 40: Computer Architecture Breakdown

## Slide 41: Computer Architecture Breakdown
Microprocessor Die

## Slide 42: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)

## Slide 43: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)
Core 1

## Slide 44: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)
Core 1
Register file
Combinational and sequential logic

## Slide 45: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)
Core 1
Register file
Core 2
Core 3
Core 4
Combinational and sequential logic

## Slide 46: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
Register file
Core 2
Core 3
Core 4
Combinational and sequential logic

## Slide 47: Computer Architecture Breakdown
Microprocessor Die
Off-chip memory
(1-transistor DRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
Core 2
Core 3
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000

## Slide 48: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
Core 2
Core 3
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000

## Slide 49: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L2 cache
(6T SRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
L2 cache
(6T SRAM)
Core 2
L2 cache
(6T SRAM)
Core 3
L2 cache
(6T SRAM)
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000

## Slide 50: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 2
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 3
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000
00111 0011 1100 1000

## Slide 51: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 2
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 3
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000
00111 0011 1100 1000
00111 0011 1100 1000

## Slide 52: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 2
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 3
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000
00111 0011 1100 1000
00111 0011 1100 1000
00111 0011 1100 1000

## Slide 53: Computer Architecture Breakdown
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 1
Code
int main(void) {
int i;
int a, b, c;
for i=0; i<5; i++ {
a = (a*b) + c;
}
}
… a = (a*b) + c; …
Register file
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 2
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 3
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 4
Combinational and sequential logic
mul temp, a, b
00111 0011 1100 1000
00111 0011 1100 1000
00111 0011 1100 1000
00111 0011 1100 1000

## Slide 54: Benefits of Computer Architecture
for(i=0; i<XSIZE; i=i+1) {
for(j=0; j<YSIZE; j=j+1) {
r = 0;
for(k=0; k<XSIZE; k=k+1) {
r = r + y[i][k] * z[k][j];
}
x[i][j] = r;
}
}
for(jj=0; jj<XSIZE; jj=jj+B) {
for(kk=0; kk<YSIZE; kk=kk+B) {
for(i=0; i<XSIZE; i=i+1) {
if((jj+B) < YSIZE) {
p = jj+B;
}
else {
p = YSIZE;
}
for(j=jj; j<p; j=j+1) {
r=0;
if((kk+B) < XSIZE) {
q = kk + B;
}
else {
q = XSIZE;
}
for(k=kk; k<q; k=k+1) {
r = r + y[i][k]*z[k][j];
}
x[i][j] = x[i][j] + r;
}
}
}
}

## Slide 55: Benefits of Computer Architecture
for(i=0; i<XSIZE; i=i+1) {
for(j=0; j<YSIZE; j=j+1) {
r = 0;
for(k=0; k<XSIZE; k=k+1) {
r = r + y[i][k] * z[k][j];
}
x[i][j] = r;
}
}
for(jj=0; jj<XSIZE; jj=jj+B) {
for(kk=0; kk<YSIZE; kk=kk+B) {
for(i=0; i<XSIZE; i=i+1) {
if((jj+B) < YSIZE) {
p = jj+B;
}
else {
p = YSIZE;
}
for(j=jj; j<p; j=j+1) {
r=0;
if((kk+B) < XSIZE) {
q = kk + B;
}
else {
q = XSIZE;
}
for(k=kk; k<q; k=k+1) {
r = r + y[i][k]*z[k][j];
}
x[i][j] = x[i][j] + r;
}
}
}
}
Chart: Matrix Multiply Run Time (1000 x 1000 matrices)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Alternative MM | 2.3974 | 2.2866 | 2.3819 | 2.3201 | 2.4045 | 2.2566 | 2.2902 | 2.4434 | 2.2991 | 2.4276
Conventional MM | 3.3316 | 3.2058 | 3.4637 | 3.5152 | 3.7471 | 3.2033 | 3.3964 | 3.3813 | 3.2304 | 3.2049

## Slide 56: Benefits of Computer Architecture
for(i=0; i<XSIZE; i=i+1) {
for(j=0; j<YSIZE; j=j+1) {
r = 0;
for(k=0; k<XSIZE; k=k+1) {
r = r + y[i][k] * z[k][j];
}
x[i][j] = r;
}
}
for(jj=0; jj<XSIZE; jj=jj+B) {
for(kk=0; kk<YSIZE; kk=kk+B) {
for(i=0; i<XSIZE; i=i+1) {
if((jj+B) < YSIZE) {
p = jj+B;
}
else {
p = YSIZE;
}
for(j=jj; j<p; j=j+1) {
r=0;
if((kk+B) < XSIZE) {
q = kk + B;
}
else {
q = XSIZE;
}
for(k=kk; k<q; k=k+1) {
r = r + y[i][k]*z[k][j];
}
x[i][j] = x[i][j] + r;
}
}
}
}
Chart: Matrix Multiply Run Time (1000 x 1000 matrices)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Alternative MM | 2.3974 | 2.2866 | 2.3819 | 2.3201 | 2.4045 | 2.2566 | 2.2902 | 2.4434 | 2.2991 | 2.4276
Conventional MM | 3.3316 | 3.2058 | 3.4637 | 3.5152 | 3.7471 | 3.2033 | 3.3964 | 3.3813 | 3.2304 | 3.2049

## Slide 57: Why is the “ugly” code faster?
Microprocessor Die
L3 cache memory (shared between cores)
(6T-SRAM)
Off-chip memory
(1-transistor DRAM)
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 1
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 2
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 3
L1 cache
(6T SRAM)
L2 cache
(6T SRAM)
Core 4
00111 0011 1100 1000
00111 0011 1100 1000
We use this (on-chip, faster) memory more efficiently
Register file
Combinational and sequential logic

## Slide 58: Goal and Philosophy
RISC-V is a Reduced Instruction Set Computer
Goal
  The main goal of the design is high performance in the execution of compiled code.
Philosophy
  The basic philosophy of MIPS is to present an instruction set that is a compiler-driven encoding of the microengine. Thus, little or no decoding is needed and the instructions correspond closely to microcode instructions.

## Slide 59: Efficient Memory Access
Effective computing is analogous to effective thinking
Source: https://www.youtube.com/watch?v=VDN1JWe3rAo
Source: https://www.youtube.com/watch?v=3l31bNE6LT0

## Slide 60: Course Topics
Instruction Set Architecture (ISA) Review
Performance
RISC-V ISA (R-type, I-type, S-type, U-type)
RISC-V Selection and Repetition (SB-type)
RISC-V Procedure Calls (UJ-type, stack, nested calls)
Pipelining

## Slide 61: Course Topics
Memory Hierarchy, Caches, Cache Performance
Virtual Memory
Out-of-order Execution
Side-channel attacks
Multicore and Parallel
Cache Coherence

## Slide 62: Course Information
CSE 30321 – Computer Architecture
  Required for CS and CPEG majors
  TuTh - 11-12:15pm in DeBartolo Hall 116
Canvas Page
  https://canvas.nd.edu/courses/82217

## Slide 63: Textbook
CSE 30321 Computer Architecture zyBook
  Sign in or create an account at https://learn.zybooks.com
  Enter zyBook code: NDCSE30321MorrisonSpring2024
  Subscribe. Cost is $97 for the semester.
Course Slack
  https://app.slack.com/client/T0HJVP8MS/C06DND1TLBY
LinkedIn
  https://www.linkedin.com/in/gregariousmatt/

## Slide 64: Office Hours
My Office Hours in 178 Fitzpatrick Hall
  M, Tu, W – 1-2pm
  Th 1-3pm
  Or by Appointment
TA Office Hours on Google Calendar
  TA hours start in Week 2

## Slide 65: Reading
15 Reading Assignments worth 100 points each
  Most due on Tuesday at 11am at the beginning of each week
First Reading Assignment due this Thursday at 11am
  Get ahead of any issues, start back in the studying habit
Let’s look at Lecture Notes and Schedule and the Reading outline

## Slide 66: zyBook
Warning: readings may be longer than in Logic Design
  Chapters tend to be longer, as do sections
  Keep an eye out for “Instructor Notes”:
    Occasionally, these will call out sections that you can skip and still receive full credit for the reading:
Sections marked optional may still be of interest

## Slide 67: Homework Assignments
12 Homework Assignments work 600 points each
Assigned every Thursday and due the following Thursday
  Except for the Thursdays prior to Exam 1 and Exam 2
Submitted to Gradescope

## Slide 68: Three Exams
Exam 1 – Take Home
  Time for 2 hours on Gradescope
  Between 2/15/24 at 12:30pm and 2/16/24 at 5:00pm
  2,000 points
Exam 2 – Take Home
  Time for 2 hours on Gradescope
  Between 3/28/24 at 12:30pm and 3/29/24 at 5:00pm
  2,500 points

## Slide 69: Three Exams
Final Exam
  In Person, Timed
  Wednesday, May 8th, 10:30am - 12:30pm
  3,000 total points
Important Information
  Review Guides posted 1 week early
  Points increase to reflect your better understanding of my Exam expectations

## Slide 70: Total Points

## Slide 71: Grade Breakdown

## Slide 72: Extension Tokens
72 hours for extensions on homework assignments
  Not reading or Exams
  Granted for instances such as illness
  Not including University-excused extensions (attending a funeral, athletics, ect.)
Automatically granted if you haven’t used
A way for me to proactively help students

## Slide 73: Out of Class Work Expectations
According to Federal Law, a "Credit Hour" is legally defined as follows:
  An amount of work that reasonably approximates not less than:
    One hour of classroom or direct faculty instruction and a minimum of two hours of out of class student work each week for approximately fifteen weeks for a semester
For this course: That is an average of 7.5 hours/week
  Last 3 years of CIF Scores: 7.4 hours
If you are struggling, find me or a TA

## Slide 74: A Good Place to Discuss AI and Coding
An old calculator gives insight into a new problem…

## Slide 75: A Good Place to Discuss AI and Coding
Someday, AI may be able to reliably develop engineering-quality code

## Slide 76: Academic Integrity
A simple rule of thumb

## Slide 77: Jog Your Memory: Think, Pair, Share
Define and differentiate between computer architecture and computer organization and give examples of each.
State and briefly describe the five stages of the RISC datapath.
What is the goal of RISC?
What is the basic philosophy of RISC?

## Slide 78: Unicorn Chaser: Last Minute!
What it’s like for the Professor when there is exactly one minute left in Lecture
Instagram Artist:
  @jakekrantz
  Source: https://www.instagram.com/p/CQPMA4qAMht/

## Slide 79: Unicorn Chaser: Last Minute!
What it’s like for the Professor when there is exactly one minute left in Lecture
Instagram Artist:
  @jakekrantz
  Source: https://www.instagram.com/p/CQPMA4qAMht/